Most of the text here is from a format description provided
by the MEDS in Ottawa.

MEDS OCEAN Data Formats  (Exchange format for the GTSPP)

The format described here is used for archiving all ocean
station data managed by Marine Environmental Data Serices,
MEDS in Ottawa, Canada, and is used as the exchange format
for the GTSPP project.  The first, the station record, contains
information pertaining to the station as a whole including
position-time co-ordinates, surface met and ocean parameters,
and a history of processing and editing for the record.  There
is one of these records for each station.  The second record
type, the profile record, contains the information about the 
profile observations made at the station.

(1) Section 1 - STATION RECORD

The format is made up of five sections.  The sections can be
described as two dimension tables or relation if one prefers to
think in terms of relation data models.  The first section or
table contains information that occurs only once per station,
including the identification and location information. 

The first section contains identifications, position and time
information for the station.  It also contains information on
the source and time of receipt of the data, flags that have been
provided during the quality control process, and stream identifi-
cation code that is used to determine whether the current version
of the data will replace one already existing in the database       
during an update.  Finally, this section contains an availability
flag that controls distribution of the data and a unique record 
identifier that is used to determine an exact match if the record
is sent to someone else for QC and is then returned.

  Section 2 - Profile Information Group

The profile information contains information about each of the         
profiles collected at the station.  The parameter NO_PROF in section
1 contains the number of occurences of this group.

  Section 3 - Surface Parameter Group

The surface parameter structure contains all data that are observed
at the surface including both oceanographic and meteorological vari-
ables.  There is one occurence of this group for each variable
observed. The parameter NPARMS in section 1 contains the number of
occurences of this grup.

The optional parameters would include such things as souncing depth,
met parameters, surface temperature, surface current speed and direc-
tion, etc.        
 
The 4 character parameter code is used to differentiate between the
variables reported in this group.  Where possible MEDS and NODC use
the first four characters of the GF3 parameter code.  All variables
are represented by real numbers and a one digit QC flag is provided.
 
  Section 4 - Surface Codes Group

The surface codes structure contains all of the information collected
at the surface but represented as alphanumerics.  There is one 
occurence of the structure for each item of information.  The parameter
NSURFC in section 1 contains the number of occurences of this group.

  Section 5 - History Group

The history group contains a history of all programs and actions
performed on the data.


(2)  PROFILE RECORD

The format is made up of two sections.  The first section contains
information that occurs only once per station and represents the
single key into the data profile.  It includes the identification,
time, datatype and segment numbers.  Section 2 consists of a single
field containing the number of depths for the profile, (No_Depths). 
Section 3 contains a variable number of data pairs.



If you have a CTD profile with 3014 data points, You can expect to
see the following fields .........


Please notice that MKEY is used to tie the profile records to the
station record.

Mkey
00000100  station record
00000101  first profile record of the first station record
00000102  2nd   "
00000103  3rd   "
00000104  4th   "
00000105  5th   "
00000106  6th   "

00000200  2nd station record
00000201  first profile record of the 2nd station record

00000300  3rd station record
00000301  first profile record of the 3rd station record

---------------------------------------
The first station record ends at byte 449.  This is because there are
130 bytes for the station record, 28 bytes for 2 profile information
groups, 60 bytes for 4 Surface Parameter groups, 105 bytes for 7 Surface
Codes groups, and 126 bytes for 3 History groups.  Knowing how many
occurences there are for each group and the total byte size for each group,
you can calculate the end of the station record.  You will know when to
read the Profile record when interogating the MKEY.....00000101.


I'm going to mail the CTD.ASC file which is the example used here.


MKEY                                  DataType 
 |                                    |
00000100  346144        93199310160210CT           0 U       0 53.3400 165.0067
                                         No_Prof
                                           | NPARMS 
                                           | | Nsurfc
                                           | | |  Num_Hist
                                           | | |  | No_Seg
                                           | | |  | | 
                                           | | |  | |Prof_Type
                                           | | |  | ||       Deep_Depth
                                           | | |  | ||       |    No_Seg
                                           | | |  | ||       |    |Prof_Type
                                           | | |  | ||       |    || Deep_Depth
                                           | | |  | ||       |    ||       |
11119940909999999999999          NOCT    A 2 4 7  3 3TEMP D5 3013 3PSAL D5 3013

Pcode Parm Q_Parm
|     |       |Pcode Parm Q_Parm
|     |       ||        |    |
|     |       ||        |    |Pcode Parm Q_Parm
|     |       ||        |    ||        |    |Pcode Parm Q_Parm
|     |       ||        |    ||        |    ||       |     |SRFC_Code
|     |       ||        |    ||        |    ||       |     ||   SRFC_Parm 
|     |       ||        |    ||        |    ||       |     ||   |  SRFC_Q_Parm
|     |       ||        |    ||        |    ||       |     ||   |         |
|     |       ||        |    ||        |    ||       |     ||   |         |SRFC_
|     |       ||        |    ||        |    ||       |     ||   |         |Code
|     |       ||        |    ||        |    ||       |     ||   |         ||
ATMS  1008.7000WETT     0.0000DRYT     0.0000WSP#    13.0000GOCRHX175     0WDR#

SRFC_Parm 
|  SRFC_Q_Parm
|         |SRFC_Code
|         ||   SRFC_Parm 
|         ||   |        
|         ||   | SRFC_Q_Parm
|         ||   |         |SRFC_Code
|         ||   |         ||   SRFC_Parm
|         ||   |         ||   |         SRFC_Q_Parm
|         ||   |         ||   |         |
|         ||   |         ||   |         |SRFC_Code
|         ||   |         ||   |         ||   SRFC_Parm
|         ||   |         ||   |         ||   |         SRFC_Q_Parm
|         ||   |         ||   |         ||   |         |SRFC_Code
|         ||   |         ||   |         ||   |         ||   SRFC_Parm
|         ||   |         ||   |         ||   |         ||   |       SRFC_Q_Parm
|         ||   |         ||   |         ||   |         ||   |         |SRFC_Code
|         ||   |         ||   |         ||   |         ||   |         ||SRFC_Par
|         ||   |         ||   |         ||   |         ||   |         ||   |
25        0QNF$00000000  0QNP$0021fb4e  0DBID          0PLAT31HX      0STAT3   
   SRFC_Q_Parm
      |
      |  PRC_Code                                  PRC_Code   
      |  |                                         |
      0NOgt141.1619940908  RCRD9999.999  9999.999NOgced1.0 19940908  RCRD9999.9
              PRC_Code
              |
99  9999.999NOqcPr1.0219940909  RCRD9999.999  9999.999


STATION RECORD
No_Prof will be set to 2 because there are two parameter profiles....
TEMP and PSAL

The first PROFILE INFORMATION Group
No_Seg  will be set to 3 because there are three profile records for
Prof_Type TEMP

The second PROFILE INFORMATION Group
No_Seg  will be set to 3 because there are three profile records for
Prof_Type PSAL

The first PROFILE RECORD
Profile_Type  TEMP
Profile_Seg  is set to 1 for the first group of 1500 data pairs
No_Depths  is set to 1500

MKEY                               DataType   Profile_Type
|                                     |             |  Profile_Seg
|                                     |             |    |No_Depths
|                                     |             |    ||
00000101  346144        93199310160210CT           0TEMP 11500

The second PROFILE RECORD
Profile_Type  TEMP
Profile_Seg  is set to 2 for the second group of 1500 data pairs
No_Depths  is set to 1500

MKEY                               DataType   Profile_Type 
|                                     |             |  Profile_Seg
|                                     |             |    |No_Depths
|                                     |             |    ||
00000102  346144        93199310160210CT           0TEMP 21500

The third PROFILE RECORD
Profile_Type  TEMP
Profile_Seg  is set to 3 for the third group of 1500 data pairs
No_Depths  is set to 14

MKEY                               DataType   Profile_Type 
|                                     |             |  Profile_Seg
|                                     |             |    |  No_Depths
|                                     |             |    |  | 
00000103  346144        93199310160210CT           0TEMP 3  14

PROFILE RECORD
Profile_Type  PSAL
Profile_Seg  is set to 1 for the first group of 1500 data pairs
No_Depths  is set to 1500

MKEY                               DataType   Profile_Type 
|                                     |             |  Profile_Seg
|                                     |             |    |No_Depths
|                                     |             |    ||
00000104  346144        93199310160210CT           0PSAL 11500

PROFILE RECORD
Profile_Type  PSAL
Profile_Seg  is set to 2 for the second group of 1500 data pairs
No_Depths  is set to 1500

MKEY                               DataType   Profile_Type
|                                     |             |  Profile_Seg
|                                     |             |    |No_Depths
|                                     |             |    ||
00000105  346144        93199310160210CT           0PSAL 21500

PROFILE RECORD
Profile_Type  PSAL
Profile_Seg  is set to 3 for the third group of 1500 data pairs
No_Depths  is set to 14

MKEY                               DataType   Profile_Type
|                                     |             |  Profile_Seg
|                                     |             |    |  No_Depths
|                                     |             |    |  |
00000106  346144        93199310160210CT           0PSAL 3  14