Document #1

      Sources, Transport, and Nutrient Environment of Toxic "Red Tide"
                 Populations in the Western Gulf of Maine

   D.M. Anderson, B. Butman, D.A. Fong, P.J.S. Franks, B.A. Keafer, W.R.
                  Geyer, T.C. Loder III, and R.P. Signell

Article from Summer 1995 "Gulf of Maine News," the Regional Association for
                 Research on the Gulf of Maine newsletter

Franks and Anderson (1992) found that the coastal current in the western
Gulf of Maine has a strong influence on the distribution and fate of a
toxic dinoflagellate, Alexandrium tamarense. They posed the "plume
advection hypothesis", which states that a source population of A.
tamarense near the mouth of the Kennebec-Androscoggen Rivers is advected
long distances along the coast by the freshwater plume of the rivers
flowing into the western Gulf of Maine. In order to test this hypothesis
and thus to better understand the coupling between dinoflagellate
distributions and physical transport processes, a team of investigators
from Woods Hole Oceanographic Institution, Scripps Institute of
Oceanography, University of New Hampshire, and the U.S. Geological Survey
performed a combined field and modeling study of the physics and
Alexandrium distribution in the western Gulf of Maine Coastal Current. This
study has been supported by the Regional Marine Research Program since
1993.

Measurements of the physics and biology were conducted during two intensive
sampling periods in the spring of 1993 and 1994. The measurements included
a total of 14 shipboard surveys on The R/V ARGO Maine, the R/V Anderson,
and the R/V Jerry Chase, as well as deployment of current meter moorings
and surface drifters, and satellite observations of sea-surface
temperature.

The pattern of river discharge was similar between 1993 and 1994, and the
wind conditions were generally similar ( Figure 1 and Figure 2 .) However
there were several strong, downwelling-favorable (northerly to
northeasterly) wind events during the period of peak river discharge in
1993, while in 1994 the winds were upwelling-favorable (southerly to
southeasterly) during the critical period of peak river discharge. This
seemingly minor difference in wind-forcing produced markedly different
plume conditions and correspondingly large differences in the number and
distribution of Alexandrium cells. In 1993, the plume generally hugged the
coast, and virtually all of the fresh water coming out of the western Gulf
of Maine rivers could be observed within the southward flowing coastal
current, which extended continuously along the coast into Massachusetts
Bay. In 1994, there were episodes of southward transport, but they were
interrupted by several upwelling events that caused the plume to spread
offshore and actually to head northeastward for several days to a week.
Much of the fresh water was transported offshore, and the salinity of the
coastal waters were considerably higher than in the spring of 1993, even
though the freshwater input was the same.

These differences in hydrographic conditions were reflected in marked
differences in the Alexandrium sp. distributions. During 1993, the plume
carried Alexandrium cells southward, consistent with the plume advection
hypothesis, and a number of coastal stations reported toxicity as the cells
contaminated the coastal monitoring stations. During 1994, the upwelling
conditions resulted in offshore transport of the early background
concentrations of Alexandrium sp., preventing the development of a
sufficient population to cause nearshore shellfish toxicity. Later, several
shellfish sites near Casco Bay also became toxic, but these outbreaks did
not persist due to the strong upwelling conditions. In 1994, no toxicity
was detected in Massachusetts Bay, suggesting that the persistent upwelling
prevented the low-level populations to the north of Cape Ann from seeding
the southern waters via advection.

One implication of these observations is that not only the seasonally
averaged forcing conditions, but also the timing of these forcing
variables, is critical in determining the transport processes and their
influence on populations. The subtle connections between run-off,
wind-forcing and toxic plankton distribution emphasizes the need for
time-dependent models that can actually account for the covariance between
the critical forcing variables and ultimately predict the occurrence of red
tides.

Several "levels" of modeling are being pursued in this project to
understand and ultimately to predict the variations of the physical regime
and the associated red tide population. A simple, two-dimensional model was
developed to examine the time-variations of offshore extent of the plume
(Fong and Geyer, 1994; Fong et al., 1995). This analysis indicates that
wind forcing is indeed the principal agent responsible for variations in
the width of the plume, but that the basic Ekman dynamics are significantly
modified by time-dependence and friction between the plume and the
underlying water.

A more computationally-intensive, 3-dimensional model is also being
implemented. This is the same model that was used by Signell and co-workers
(e.g., Signell et al., 1993) to simulate the flow in Massachusetts Bay. The
western Gulf of Maine domain extends from Penobscot Bay to Cape Cod and out
to the 100 m isobath. One of the difficulties of implementing a "limited
domain" model such as this is the specification of the open boundary
condition. We are using the output of a larger scale model of the entire
Gulf (Namie et al., 1994) to "drive" the open boundary. Another critical
issue is the parameterization of vertical mixing, which is accomplished by
a second-order turbulence closure scheme (Mellor and Yamada, 1982). The
idealized, two-dimensional model indicated that friction was important,
implying turbulence in the stratified shear layer at the base of the plume.
The comparison between the 3-D model and observations show discrepancies
that may be explained by an underestimate of the friction term. This study
of the turbulence parameterization of the model is important both for the
predictive skill of this model and for the general problem of mixing in
river plumes.

In addition to these physics-oriented model studies, we are also modeling
the coupled physics-biology problem ( Figure 3). So far, our simulations
have addressed the advection and growth of cells, with a simple,
temperature-dependent growth function. These runs have shown that nature is
more complicated than the model. One of the difficulties is adequately
parameterizing the source function, which we believe to originate from a
"seed population" of cysts in the bottom sediments near the mouth of the
Kennebec River. Other questions involve the role of physical aggregation at
fronts (Franks, 1992), the influence of nutrients on growth, and predation.
Ultimately, this coupled modeling effort will lead to a better
understanding of the dynamics of the Alexandrium population as well as a
potential predictive tool for forecasting "red tide" outbreaks.

References

Fong, D.A., Geyer, W.R, and R.P. Signell, 1995. Ekman dynamics of the
western Gulf of Maine plume. Journal of Marine Systems, submitted.

Fong, D.A., and W.R. Geyer, 1994. Wind-forcing of river plumes. American
Geophysical Union Fall Meeting, San Francisco, CA. Abstract: EOS
Supplement, 75: 052-7.

Franks, P.J.S., 1992. Sink or swim: accumulation of biomass at fronts.
Marine Ecology Progress Series, 82:1-12.

Franks, P.J.S. and D.M. Anderson, 1992. Alongshore transport of a toxic
phytoplankton bloom in a buoyancy current: Alexandrium tamarense in the
Gulf of Maine. Marine Biology, 112:153-164.

Mellor, G.L. and T. Yamada, 1982. Development of a Turbulence Closure Model
for Geophysical Fluid Problems, Review of Geophysical Space Physics, 20:
851-875.

Naimie, C.E., Loder, J.W., and D.R. Lynch, 1994. Seasonal-Variation of the
3-Dimensional Residual Circulation on Georges Bank, J. of Geophysical
Research-Oceans, 99(8): 15967-15989.

Signell, R.P., Jenter, H.L., and A.F. Blumberg, 1994. Modeling the Seasonal
Circulation in Massachusetts Bay, Proceedings of the 3rd International
Conference on Estuarine and Coastal Modeling III, Publ by ASCE, NewYork,
NY, USA., p 578-590.




Document #2


      Sources, Transport, and Nutrient Environment of Toxic "Red Tide"
                 Populations in the Western Gulf of Maine

   D.M. Anderson, B. Butman, D.A. Fong, B.A. Keafer, P.J.S. Franks, W.R.
                  Geyer, T.C. Loder III, and R.P. Signell

                 November 1996 Progress Report to the RMRP

During the last six months, we continued to work on the synthesis of data
collected during the 1993 and 1994 field seasons. Although some raw data is
still being generated (e.g., cell counts of Alexandrium ), more effort has
gone into merging datasets and working on interpretation of the results.
For example, the nutrient fields were integrated with the cell counts and
hydrographic data using Matlab software. This required that some project
staff work closely with other team members who were not as familiar with
the complexities of Matlab.

Results of the project continue to be presented at conferences and
workshops. B. Keafer and C. Martorano attended the biannual Maine Biotoxin
workshop in October at the Maine Dept. of Natural Resources in Boothbay
Harbor, ME where shellfish managers and other regulatory officials were
given updates on the project during open discussions. The animations of the
hindcast simulations for both 1993 and 1994 (available on the Web) were
presented on videotape for attendees. Other presentations on the project
were by D.M. Anderson at a NOAA workshop on Management and Mitigation of
Harmful Algal Blooms, held in Seattle in September, and at a NATO Advanced
Study Institute on the Physiological Ecology of Harmful Algal Blooms, held
in Bermuda in May.

Progress within each of the project elements is given below:

Nutrients and cell counts

Significant progress has been made in merging the Alexandrium cell count
data with the nutrient data, enabling a comparative analysis. Nutrient
samples (approx. 2000) from the 1993 and 1994 field seasons have been
analyzed and finalized for nitrate, nitrite, phosphate, ammonium, and
silicate (1993) and nitrate+nitrite, phosphate, ammonium, and silicate
(1994). Contour plots of surface (3 m) nutrient concentrations and DIN have
been created to match with the accompanying surface contours of Alexandrium
. These plots and analyses of the nutrient data relative to the occurrence
of Alexandrium blooms are the subject of C. Martorano's Master's thesis at
the University of New Hampshire which will be completed early in 1997.

At this time, data analysis suggests that the major sources of nutrients to
the surface waters of the southwestern coastal Gulf of Maine are: the
Kennebec/Androscoggin freshwater plume, the Eastern Maine Coastal Current,
wind-induced upwelling; tidally-driven wave-sill interaction on Stellwagen
Bank, local river inputs (such as the Merrimack), and sewage effluent from
Boston Harbor.

Initial analysis also indicates that the occurrence and persistence of red
tide blooms in the southwestern Gulf of Maine is not a result of inorganic
nutrient enrichment. The toxic Alexandrium blooms typically occurred during
the late spring after nutrients in the coastal current were well depleted
by early spring phytoplankton blooms mainly consisting of diatoms. In
particular, the highest Alexandrium cell concentrations observed during the
1993 and 1994 sampling seasons (907 and 908 cells/liter) were measured in
waters which contained DIN levels of 0.30 and 0.73 , respectively. These
low nitrogen levels indicate that the nitrogen was already ``stripped''
from the surface waters by the earlier diatom bloom. It is unlikely that
Alexandrium itself, as only a minor component of the phytoplankton
community, could have a major impact on the nutrient concentrations. We
hypothesize that Alexandrium survives due to its ability to grow at very
low levels (0-1 ) of DIN concentrations, and/or by its ability to obtain
nitrogen from the pycnocline region of the water column through vertical
migration. We suspect that once established at low levels, Alexandrium
could grow rapidly if it were transported into an area rich in nutrients
caused by upwelling, vertical mixing, or anthropogenic inputs. However,
upwelling is not conducive to the nearshore accumulation of Alexandrium
(see below), so the latter two mechanisms may be more important to bloom
development and maintenance. This dinoflagellate seems to have excellent
capability for adaptation, and does not appear to be constrained by its
chemical environment. Thus, the physical environment may have been the more
dominant factor regulating the distribution of Alexandrium in the
southwestern Maine coastal current during 1993 and 1994.

Hydrography and modeling

The hydrography and moored current meter data have been analyzed to better
understand the alongshore transport of the freshwater and Alexandrium .
(Geyer et al., 1997) The structure of the plume is strongly influenced at
short time scales by fluctuations in wind stress; however the wind stress
is not the dominant contributor to the net transport of the plume. A
persistent, along-coast, barotropic current is the biggest contributor to
the plume transport, exceeding the contribution of the baroclinic flow due
to the density anomaly of the plume itself.

Another important implication of the physical observations is that the
timing of forcing conditions is critical in determining the transport and
fate of the plume. Meteorological records show variability in both wind
speed and direction over time scales of a few days. Winds fluctuate between
upwelling, downwelling, and neutral conditions; the longer time-scale
(monthly) averaged wind stress is nearly zero. Analysis of the observations
from the spring freshets of 1993 and 1994 (Fong et al. 1996; Geyer et al.,
1997) emphasize that the local winds are responsible for plume variability
over short time scales unresolved by the hydrographic surveys.

The effects of transient wind events on mixing the freshwater plume are
being investigated using a three-dimensional numerical model. This is a
simplified version of the Blumberg-Mellor model used by Signell et al.
(1994) in studying flows in Massachusetts Bay. The model is forced by a
point source of freshwater and different wind forcing conditions. These
idealized modeling studies aim at learning about the plume's behavior in
the presence of fluctuations in wind stress.

As a generalization of the wind conditions present in the western Gulf of
Maine, initial experiments were conducted by forcing the model with
sinusoidally varying (in time) wind stresses of different amplitudes. These
experiments demonstrated that even with a zero temporal mean wind stress,
wind fluctuations result in significant mixing of the plume. As illustrated
by Figure 1 , moderate winds of amplitude 0.5 are capable of causing
significant ``dispersal'' of the freshwater in comparison to the zero wind
forcing case. Strong wind fluctuations of amplitude 1.0 dramatically mix
the freshwater with the ambient coastal water; in particular, strong
sustained upwelling fluctuations appear capable of strongly mixing the
plume such that the freshwater signal of the plume is largely removed.

More detailed and quantitative analyses are being conducted to investigate
the role of individual upwelling and downwelling favorable wind events.
Strong upwelling and downwelling winds are both capable of initiating
significant mixing between the plume and ambient coastal waters.
Downwelling winds compress the plume against the coast which results in a
reduction in overall stratification; the reduced stratification, coupled
with enhanced shears in the alongshore velocity field promotes enhanced
mixing through shear instability processes. Upwelling winds, in contrast,
spread and advect the plume offshore consistent with Ekman drift theory
(see Fong et al., 1996); the associated shears with the cross-shore Ekman
transport work against the stratification and enhance mixing.

Detailed analyses of the cumulative vertical buoyancy flux and salinity
distributions show that upwelling winds are more effective at mixing the
plume than comparable magnitude downwelling favorable winds. (Figure 2).
The differences in mixing rates between the two wind conditions is
attributable to differences in wind energy available for mixing the plume.
Upwelling winds broaden the plume in cross-shore extent thereby providing a
large surface area over which the wind's energy can be input into the
mixing the plume. In contrast, the downwelling winds which push the plume
tightly against the coast, decrease the surface area over which the wind
can act to mix the plume and ambient coastal waters. The large differences
in plume surface area for the different wind conditions result in at least
twice, often three times, greater mixing rates for upwelling favorable wind
conditions.

While these modeling exercises are simplified idealizations of the real
western Gulf of Maine plume system, many important physical processes have
been identified. The model runs clearly demonstrate that the temporal
variability of winds is responsible for significant changes in plume
structure and transport over time scales as short as a few days. Strong
wind events, particularly upwelling favorable, appear capable of enhancing
mixing to levels such that the alongshore transport of plume waters is
strongly retarded, and the freshwater and Alexandrium are significantly
dispersed in both the cross-shore and vertical directions. Given the
combination of both elevated mixing rates and temporarily arrested of the
downcoast transport, upwelling winds seem most capable of dispersing
concentrations of Alexandrium cells. It seems likely that for sufficiently
strong upwelling wind events, the downstream transport of freshwater and
toxic cells may be greatly reduced; mixing will dramatically reduce the
baroclinically-driven flow and make the ambient current the only major
agent capable of net plume transport. The idealized simulations also
emphasize that the timing of cell release with respect to wind events is
critical in predicting algal bloom dynamics.

Studies are continuing with the idealized model to identify the locations
of strongest mixing during large wind events. Preliminary results suggest
intensified mixing occurs at the offshore edge of the plume. This behavior
would suggest that red tide cell growth may be largest in the frontal
regions of the plume given the elevated fluxes of nutrients associated with
the amplified mixing. However, any increases in the population density due
to growth at the offshore mixing zone may be outweighed by subsequent
dispersion of the population during strong upwelling conditions. This also
emphasizes the need to understand the timing and source conditions
associated with release of toxic cells. The combined timing of buoyancy and
wind forcing and cell release will determine the ultimate toxicity and
location of high concentrations.

In addition to the idealized modeling, we have also numerically hindcasted
the 1993 and 1994 field seasons using realistic bathymetry, measured wind,
river and heat flux data, and boundary conditions derived from in situ
observations. In these simulations we seek to determine the degree to which
three-dimensional models can ``recreate'' the observed field data and,
based on this determination, use the models to address issues that are
unresolved by the field data.

One of the main hypothesis we tested with the hindcast simulations was that
it was the differences in local wind forcing and river discharge between
1993 and 1994 were sufficient to explain the large differences in
Massachusetts toxicity that was observed between these two years. In both
years, however, the hindcast simulations show freshwater lenses containing
Alexandrium cells working their way into Massachusetts Bay where the cells
experience in situ growth due to warm water temperatures and relatively
long residence times. This suggests that toxicity in Massachusetts cannot
be attributed to physical variability of the wind and river discharge
alone, but is dependent on biological variability as well.

One of the certain causes of biological variability is in the actual
process by which the cells move from the cysts in the sediment into the
fresh plume waters. In the hindcast simulations, however, cells were
introduced in the river water with the same fixed concentration for both
years. Had the fresh water lens that moved into Massachusetts Bay during
1994 contained no cells, the model would not have predicted toxicity. The
simulations show that our present formulation of the source condition for
the cells is much too simplified. A more accurate source condition, based
on a better understanding of the process by which cells germinate and are
transported to the surface waters, would allow a time variable source
condition for cells that could explain the toxicity differences between
1993 and 1994. Without better understanding of the source conditions,
however, it is not clear that further progress can be made in the
hindcasting or prediction of red-tides in this region. We expect to pursue
this level of detail in a forthcoming proposal to study the initiation zone
in another large-scale Alexandrium study in the Gulf of Maine.

References

Fong, D.A., Geyer, W.R. and R.P. Signell, 1996. The wind-forced response on
a buoyant coastal current: Observations of the western Gulf of Maine plume.
Journal of Marine Systems, in press.

Geyer, W.R., Signell, R.P, Fong, D.A., Wang, J., Anderson D.M., and B.A.
Keafer, 1997. The Kennebec River plume and the coastal current of the
western Gulf of Maine, in prep.

Signell, R.P., Jenter, H.L., and A.F. Blumberg, 1994. Modeling the Seasonal
Circulation in Massachusetts Bay, Proceedings of the 3rd International
Conference on Estuarine and Coastal Modeling III, Publ by ASCE, NewYork,
NY, USA., p 578-590.