NOAA Ship KA‘IMIMOANA - R333

                           [NOAA Ship KA'IMIMOANA]
----------------------------------------------------------------------------

Near Real-time images and data from the KA‘IMIMOANA.

Be sure to visit the KA‘IMIMOANA's "at sea" website for near real-time
images and data from the ship. This site features daily updates of the
ship's position & trackline, weather and sea conditions, and a whole lot
more.

----------------------------------------------------------------------------

Operational Missions

The KA‘IMIMOANA (The Ocean Seeker) is the newest addition to the fleet of
vessels used by the National Oceanic and Atmospheric Administration (NOAA)
to improve our nations' understanding of the physical environment. The
KA‘IMIMOANA, will be utilized primarily by NOAA's office of Ocean and
Atmospheric Research (OAR) and operated by the Office of NOAA Corps
Operations.

KA‘IMIMOANA was originally built as the U.S. Naval Ship TITAN (T-AGOS 15) in
1989 by Halter Marine in Moss Point, Mississippi. TITAN was operated by the
Military Sealift Command as an Ocean Surveillance Ship until her transfer to
NOAA on August 31, 1993. Conversion to her present configuration began in
May, 1995 at Maritime Contractors, Inc Shipyard in Bellingham, Washington,
and, she was redelivered to NOAA as KA‘IMIMOANA in April 1996. KA‘IMIMOANA
is now fully operational, ready to support NOAA's oceanographic and climate
research missions in the Pacific.

KA‘IMIMOANA will primarily be involved in the Global Ocean Atmosphere Land
System (GOALS) and the Pan American Climate Studies (PACS) research
programs, part of NOAA's Tropical Atmosphere-Ocean (TAO) mission. These
programs are designed to improve our understanding of the role of the
tropical ocean in modifying the world's climate. The ship will deploy,
recover, and service deep sea moorings that measure ocean currents, ocean
temperatures, and atmospheric variables throughout the equatorial Pacific
Ocean (see TAO Array location map). In addition to buoy measurements, which
are transmitted in real time to the NOAA Pacific Marine Environmental
Laboratory (PMEL) in Seattle, the ship will measure upper ocean currents,
surface salinity, carbon dioxide content,and upper air atmospheric soundings
while underway. A census of barnacles and marine life that inhabit the
recovered moorings and the periodic replacement of undersea hydrophone
moorings used to locate undersea spreading centers and hydrothermal vents on
the East Pacific Rise will also be conducted on an on-going basis.

----------------------------------------------------------------------------

Vessel Photos and Line Drawings

   * KA‘IMIMOANA casting off the last line as it departs for its first
     cruise (79k)
   * KA‘IMIMOANA Departing Seattle, WA, on first cruise (38k)
   * Inboard Profile (37k)
   * Deck Plan: Navigation Bridge (9k)
   * Deck Plan: Upper Deck (38k)
   * Deck Plan: Forcastle Deck (42k)
   * Deck Plan: Main Deck (35k)
   * Deck Plan: Lower Platform (27k)
   * Deck Plan: Hold (16k)

----------------------------------------------------------------------------

[Image]

Ship Specifications

LAUNCHED: 1988                         HULL: Welded steel/ice strengthened
DELIVERED: 1989                        DISPLACEMENT: 2,300 tons
COMMISSIONED: May 1996                 GROSS TONNAGE: 1,522
CALL LETTERS: WTEU                     NET TONNAGE:  1,034

                                       LENGTH (LOA): 224 ft. (68.3 m)
BUILDER: Halter Marine                 BREADTH (moulded): 43 ft. (13.1 m)
         Moss Point, MS                DRAFT, MAXIMUM: 15 ft. (4.6 m)
HOME PORT: Honolulu, HI

CRUISING SPEED: 10.5 knots             RANGE: 8,000 nmi
POWER: 1,600 SHP                       FUEL TYPE: #2 diesel
FUEL CAPACITY: 116,000 gal.            FUEL CONSUMPTION: 35/gal/hr/generator
ENDURANCE: 30 days                     ENDURANCE CONSTRAINT: Stability

Habitability

BERTHING                               FOOD-SERVICE SEATING
CAPACITY
Single staterooms: 21                  Forward Mess:  8
Double staterooms: 6                   Aft Mess:  16
Total bunks: 33

[Image]

Scientific Laboratory Facilities

Lab Space: 950 sq. ft.

Complement

Commissioned officers: 5               Licensed engineers: 3
(Including 1 USPHS Officer)
Crew: 13                               Scientists: 12

Medical Facilities

Medical Treatment Room with one bunk; one USPHS medical technician.

Electronics

COMMUNICATIONS
VHF/FM transceivers                    HF transceivers
Portable emergency transceiver         Weather facsimile receiver
Emergency radio auto alarm             SITOR/PACKET/RTTY modems
EPIRB's                                INMARSAT standard A system
NAVTEX receivers                       INMARSAT standard C system
Cellular Telephone                     High speed/multi-baud rate modems
Secure Telephone                       AFARTS receiver

ACOUSTICS
Deep Water Echo Sounder                Shallow water echo sounder
Doppler Speed Log

NAVIGATION
Radars (X- and S-band)                 Gyrocompass
LORAN C receivers                      C/A code, DGPS receivers
Radio Direction finder                 Acoustic Navigation (short baseline)
SATNAV                                 Omega

SCIENTIFIC EQUIPMENT
CTD system                             XBT system
Shipboard Environmental Acquisition System (SEAS)

[Image]

Data Acquisition and Processing System

The KA‘IMIMOANA is outfitted with an upgraded oceanographic system. This
system is referred to as the Scientific Computer System (SCS). The SCS
consists of two networked DEC Alpha computer systems that provide both data
acquisition and data processing functions. One Alpha is dedicated to
acquire, log, and display data in real-time, as well as perform real-time
data quality assurance functions. The second Alpha is dedicated to shipboard
scientists for data analysis and their research.

[Image]

----------------------------------------------------------------------------

KA‘IMIMOANA's Schedule

KA‘IMIMOANA's E-mail address is: Postmaster.Kaimimoana@noaa.gov

KA‘IMIMOANA's Mail address is:

     NOAA Ship KA‘IMIMOANA
     No. 1 Sand Island Road
     Honolulu, HI 96819-2222

KA‘IMIMOANA's telephone numbers in Honolulu are:

     808-471-7538, 7539, 7534, 7536
     808-471-7537, CO
     808-471-7535, FAX

Return to Marine Operations Home Page
Inquires and Comments

                 URL: http://www.pmc.noaa.gov/ka/index.html
                              Updated: 03/06/97