Dive 4246		18 Sept 2006

Pilot: Gavin Eppard

Observers: Keir Becker (port), Jon Rice (stbd)

~1540	launch

1615	cementer reported 40 m from 1301B, after 85m/min descent

1723	sub at bottom; port weight stuck; sub into muddy bottom

x 2686	y 5701

1739	weight still not released, remove 4 plates on basket

1745	pump out VB

1806	neutral at VBP 2073psi, VPwt 116; x 2577 y 5866

1820	cementer in sight; check ropes first

1839	descent weight off

1841	1 plate off cementer

1845	forks engaged, make sub light

1848	VBP 2080 psi, VBwt 108 VBT 1.8C

1859	land cementer on platform, valve wrong side, spin unit

1910-21	pull blue line and attach to wellhead

1929	change tapes

1956	white line cut

2040	cementing hose in place

2041	pin removed from cementing piston

2057	pin removed from valve lever handle

2058	valve opened, but plunger not moving; tap/bang plunger, shake unit, no joy

2115	cycle valve

2117 	no joy

2127	attach red hook to D-ring at wellhead

2135/36	pull two weights from cementer into basket

2150 cut blue line, cementer just cleared well head